## Slide 1
人形机器人 RL 部署运行时架构与数据流
实机 RL_solver 与 MuJoCo sim2sim 共用 IntegratedControllerRuntime / RL_controller 控制核心
外部输入与配置资产
共享策略控制核心
执行后端与可观测输出
操作员 GUI / 脚本
humanoid_ops_gui.py、手柄、shell 工具
DDS / ROS 2 控制话题
/humanoid/rl/teleop /humanoid/rl/mode_control
IMU 输入
/imu/yesense 仅实机路径使用
模式与机器人配置
rl_cfg.yaml + profiles/*.yaml 关节顺序、增益、限幅、策略组
观测清单
observation_manifest_*.yaml 观测项顺序与维度合同
策略资产
policies/*.onnx
参考轨迹 / 外部特征
ReferenceMotionProvider ExternalObservationProvider
ModeProfileRegistry
一次性加载 deploy_mode_profiles 按 mode 解析 config_section
IntegratedControllerRuntime
缓存最新 teleop 与 mode 命令 计算 phase_t，调用控制器 step
RL_controller::step
更新状态/命令、模式切换、观测构造、策略推理、命令组装
DeployStateMachine
回零、启动、停止、急停 解析 mode/lifecycle 控制字
当前 ModeProfile
obs/action/reference 关节合同 policy adapter 与 strategy 设置
ObservationFeatureContext
RobotState + teleop + phase_t last_action + 参考/外部特征
ObservationBuilder
按 manifest 注册表拼接 确定性的 obs 向量布局
观测历史
obs deque stacked observation buffer
PolicyInferenceStrategy
sync weighted 或 chunked receding
OnnxPolicyAdapter
统一策略后端接口
OnnxPolicyRunner
ONNX Runtime 推理 action + 可选 extra outputs
RobotCommandData
目标 q、力矩、增益 runtime command mode
实机路径
RL_solver / RobotSolver DDS 输入缓存、电机状态读取、HOLD 处理
电机共享内存 I/O
MotorShmIo + 运动学转换 读关节反馈 / 写目标与力矩
机器人电机与传感器
joint q/dq、力矩、状态
MuJoCo sim2sim 路径
mujoco_sim_bridge C++ 后端 从 qpos/qvel/base/body 构造 RobotState
MuJoCo 执行器写回
策略关节 + HOLD 关节 mj_step / hold
查看器 / 前端镜像
GLFW 或 Python viewer 话题
可观测输出
/humanoid/rl/state viewer_frame / inspector runtime log / MCAP
速度 + 模式
模式合同
观测合同
模型文件
参考/传感特征
RobotState + 输入
obs 向量
推理
action
控制命令
关节反馈
遥测/日志
蓝色：状态/观测数据
紫色：策略推理链
橙色：控制命令
虚线：遥测/日志/反馈

## Slide 2
Humanoid RL Deploy Runtime Architecture and Data Flow
Real-robot RL_solver and MuJoCo sim2sim share IntegratedControllerRuntime / RL_controller
External Inputs and Assets
Shared Policy-Control Core
Execution Backends and Observability
Operator GUI / Scripts
humanoid_ops_gui.py, joystick, shell tools
DDS / ROS 2 Control Topics
/humanoid/rl/teleop /humanoid/rl/mode_control
IMU Input
/imu/yesense real robot path only
Mode and Robot Config
rl_cfg.yaml + profiles/*.yaml joint order, gains, limits, policy groups
Observation Manifests
observation_manifest_*.yaml term order and feature dimensions
Policy Assets
policies/*.onnx
Reference / External Features
ReferenceMotionProvider ExternalObservationProvider
ModeProfileRegistry
loads deploy_mode_profiles once resolves config_section per mode
IntegratedControllerRuntime
caches latest teleop and mode command computes phase_t, calls controller step
RL_controller::step
state/command update, mode switch, observation build, policy inference, command assembly
DeployStateMachine
zero, start, stop, e-stop mode/lifecycle control words
Active ModeProfile
obs/action/reference joint contracts policy adapter and strategy settings
Observation Feature Context
RobotState + teleop + phase_t last_action + reference/external features
ObservationBuilder
manifest registry assembly deterministic obs vector layout
Observation History
obs deque stacked observation buffer
PolicyInferenceStrategy
sync weighted or chunked receding
OnnxPolicyAdapter
backend-neutral policy interface
OnnxPolicyRunner
ONNX Runtime inference action + optional extra outputs
RobotCommandData
target q, torque, gains runtime command mode
Real-Robot Path
RL_solver / RobotSolver DDS input cache, motor state read, HOLD handling
Motor Shared Memory I/O
MotorShmIo + kinematic conversion read joint feedback / write targets and torque
Robot Motors and Sensors
joint q/dq, torque, status
MuJoCo Sim2Sim Path
mujoco_sim_bridge C++ backend builds RobotState from qpos/qvel/base/body
MuJoCo Actuator Writeback
policy joints + HOLD joints mj_step / hold
Viewer / Frontend Mirror
GLFW or Python viewer topics
Observable Outputs
/humanoid/rl/state viewer_frame / inspector runtime log / MCAP
velocity + mode
mode contract
obs contract
model file
reference/sensor features
RobotState + inputs
obs vector
inference
action
control command
joint feedback
telemetry/logs
Blue: state/observation data
Purple: policy inference chain
Orange: control commands
Dashed: telemetry/logging/feedback